Two-wire transmission lines
Outline:
What is the purpose of this study?
What and how was done in the study?
What are possible future directions for the study?

---
Why study it?
- Two-wire transmission lines are most common today
- Have a simple structure
- Therefore there are not so many dependencies for the parameters
- However, due to the first point, this topic is of great interest and is not extremely complex as a result

---
What we get from this study
- Understanding of how parameters of the line affect it's characteristics
- Can we use analytical formula in case parameters of the line are equal to certain value?
- Basic skills of using simulation software
  (COMSOL, for instance), although that was not the main point of the study

---
Example:
Two plate transmission line
- Problems:
  - Plates are infinitely thin
  - Simulation mesh might get very big
- Solutions:
  - Define boundaries of inner square (or rectangle) as conductors
  - Pick appropriate size by trial and error, so that the simualtion results do not change drastically, compared with previous values

---
Calculating impedance
- We need L and C of the line
  - They are the part of the energy equations
  - Calculate them using these equations:
L = 2W_m over I^2
U = 2W_e over U^2
Optimization: set 1 for current and voltage in the simulation parameters

---
Calculating impedance...
The only step that is left now is:
Z = sqrt{L over C} = sqrt{2W_m over 2W_e} = sqrt{W_m over W_e}
- Then we can calculate the analytical function and compare the plots of two solutions
- In the formula above we consider I = 1A and U = 1V

---
Two parallel plates
- Consider following:
  - We have two infinitely thin plates of width w
  - They are separated by b meters of insulator
  - Let insulator be air
  - How impedance of such structure can be calculated?
  - Analytic formula:
Z approx %eta {b} over {w}
Fig. 1: Cross section of the line

---
Calculation results

---
Simulation screens
Fig. 2: Electric potential and its density in the two plate transmission line.
Fig. 3: Magnetic flux and its density in the two plate transmission line.

---
Some conclusions on case
- It can be seen from plot that the analytical formula is not always correct
- The bigger the plate width gets, the more accurate our estimation becomes
- The analytical formula approaches values of simulation, meaning that the error is decreasing and consequently getting closer to actual value

---
Wire above groung plane
Consider the following:
- An infinite charged plane
- A cable of diameter d above that plane
- Distance from center of the cable to the surface of the plane is h.
- Analytical formula for the impedance:
Z = %eta over {2 %pi} log{4h over w}
Fig. 4: Cross section of the line

---
Simulation and analytical solution

---
Future directions
- Fix simulations that were done improperly
- Make a proper report
- Reviev other cases (Shielded pair, for instance)
- Review different dielectrics (polyethylene, rubber)

---
COMSOL TIME
- Show some parts of the models in COMSOL
- Questions?