Two-wire transmission lines
Outline:
What is the purpose of this study?
What and how was done in the study?
What are possible future directions for the study?
Gianfranco Scordino
Ponomarenko-Timofeev Aleksei

---
Why study it?
- Two-wire transmission lines are most common today
- Have a simple structure
- Therefore there are not so many dependencies for the parameters
- However, due to the first point, this topic is of great interest and is not extremely complex as a result

---
What we get from this study
- Understanding of how parameters of the line affect it's characteristics
- Can we use analytical formula in case parameters of the line are equal to certain value?
- Basic skills of using simulation software
  (COMSOL, for instance), although that was not the main point of the study

---
Parallel Plate Transmission Line
Parallel plate transmission line,
theory
alignl { stack { size 12{"Assume "e rSup { size 8{ - jβz} } " variation, no variation with "x} {} # "TM modes: " nabla rSub { size 8{t} } rSup { size 8{2} } e rSub { size 8{z} } +k rSub { size 8{c} } rSup { size 8{2} } e rSub { size 8{z} } =0" , "k rSub { size 8{c} } rSup { size 8{2} } = left lbrace matrix { k rSub { size 8{0} } rSup { size 8{2} } -β rSup { size 8{2} } " in the air region" {} ## k rSup { size 8{2} } -β rSup { size 8{2} } " in the dielectric region" } right none {} # "Let "k rSub { size 8{c} } = left lbrace matrix { p" for air region" {} ## ℓ" for the dielectric region" } right none {} # ℓ rSup { size 8{2} } - p rSup { size 8{2} } = \( ε rSub { size 8{r} } - 1 \) k rSub { size 8{0} } rSup { size 8{2} } {} # {} } } {}

---
PowerPoint Presentation
alignl { stack { size 12{h rSub { size 8{x} } \( y \) = left lbrace matrix { { {jε rSub { size 8{r} } k rSub { size 8{0} } Y rSub { size 8{0} } } over {ℓ rSup { size 8{2} } } } { { partial e rSub { size 8{z} } } over { partial y} } " For dielectric region" {} ## { { ital "jk" rSub { size 8{0} } Y} over {p rSup { size 8{2} } } } { { partial e rSub { size 8{z} } } over { partial y} } " for air region" } right none } {} # e rSub { size 8{z} } \( y \) =C rSub { size 8{1} } "sin"ℓy" "0 <= y <= a {} # e rSub { size 8{z} } \( y \) =C rSub { size 8{2} } "sin"p \( b - y \) " "a <= y <= b {} # C rSub { size 8{1} } "sin"ℓa =C rSub { size 8{2} } "sin" ital "pc" {} # { {ε rSub { size 8{r} } } over {ℓ} } C rSub { size 8{1} } "cos"ℓa = - { {1} over {p} } C rSub { size 8{2} } "cos" ital "pc" {} # ℓ"tan"ℓa= - ε rSub { size 8{r} } p"tan" ital "pc"" Transcedental equation must be solved " {} # "simultaneously with "ℓ rSup { size 8{2} } - p rSup { size 8{2} } = \( ε rSub { size 8{r} } - 1 \) k rSub { size 8{0} } rSup { size 8{2} } " " drarrow ℓ,p {} # {} # {} } } {}

---
alignl { stack { size 12{β= sqrt {k rSub { size 8{0} } rSup { size 8{2} } - p rSup { size 8{2} } } = sqrt {k rSup { size 8{2} } - l rSup { size 8{2} } } } {} # "Most of the modes will be nonpropagating if "β" is imaginary" {} # "The variation is "e rSup { size 8{ - lline β rline z} } " and the field decays exponentially" "." {} } } {}
alignl { stack { size 12{"The value of "β" between "k rSub { size 8{0} } " and "k" can occur if "p= ital "jp" rSub { size 8{0} } } {} # "Let "ℓ rSub { size 8{0} } " to be the corresponding value of "ℓ" then:" {} # ℓ rSub { size 8{0} } "tan"ℓ rSub { size 8{0} } a=ε rSub { size 8{r} } p rSub { size 8{0} } "tan"p rSub { size 8{0} } c {} # ℓ rSub { size 8{0} } rSup { size 8{2} } +p rSub { size 8{0} } rSup { size 8{2} } = \( ε rSub { size 8{r} } - 1 \) k rSub { size 8{0} } rSup { size 8{2} } {} } } {}

---
Low Frequency Solution
Low Frequency Solution
When the frequency is low,
alignl { stack { size 12{k rSub { size 8{0} } rSup { size 8{2} } " is very small number , "ℓ rSub { size 8{0} } " and "p rSub { size 8{0" "} } "are very small " drarrow } {} # ℓ rSub { size 8{0} rSup { size 8{2} } } a=ε rSub { size 8{r} } p rSub { size 8{0} } rSup { size 8{2} } c {} # \( ε rSub { size 8{r} } - 1 \) k rSub { size 8{0} } rSup { size 8{2} } - p rSub { size 8{0} } rSup { size 8{2} } = { {ε rSub { size 8{r} } p rSub { size 8{0} } rSup { size 8{2} } c} over {a} } {} # "or "p rSub { size 8{0} } rSup { size 8{2} } = { { \( ε rSub { size 8{r} } - 1 \) k rSub { size 8{0} } rSup { size 8{2} } a} over {a+ε rSub { size 8{r} } c} } " The solution for "β" is" {} # β= sqrt {k rSub { size 8{0} } rSup { size 8{2} } +p rSub { size 8{0} rSup { size 8{2} } } } = sqrt { { {ε rSub { size 8{r} } b} over {a+ε rSub { size 8{r} } c} } " "} k rSub { size 8{0} } = sqrt {ε rSub { size 8{e} } } k rSub { size 8{0} } {} # ε rSub { size 8{e} } " is the effective dielectric constant" {} } } {}

---
y
b
x
-W
W
alignl { stack { size 12{ε rSub { size 8{e} } =ω sqrt {LC} " "L,C" are the static inductance and capacitance "} {} # "per meter" "." {} # "The time average stored magnetic energy is "W rSub { size 8{m} } {} # W rSub { size 8{m} } = { {μ rSub { size 8{0} } } over {4} } Int rSub { size 8{0} } rSup { size 8{b} } { Int rSub { size 8{ - w} } rSup { size 8{w} } {H rSub { size 8{x} } rSup { size 8{2} } } } ital "dxdy"= { {μ rSub { size 8{0} } } over {2} } ital "WbJ" rSub { size 8{z} } rSup { size 8{2} } = { {1} over {4} } ital "LI" rSub { size 8{z} } rSup { size 8{2} } {} # I rSub { size 8{z} } =2 ital "WJ" rSub { size 8{z} } " " drarrow L= { {μ rSub { size 8{0} } b} over {2W} } {} # {} } } {}

---
alignl { stack { size 12{C rSub { size 8{2} } =C rSub { size 8{1} } "sin"ℓ rSub { size 8{0} } a/j"sinh"p rSub { size 8{0} } c approx - ital "jC" rSub { size 8{1} } βℓ rSub { size 8{0} } a/p rSub { size 8{0} } c} {} # 0 <= y <= a {} # e rSub { size 8{z} } =C rSub { size 8{1} } ℓ rSub { size 8{0} } y {} # e rSub { size 8{y} } = - { {jβ} over {ℓ rSub { size 8{0} } } } C rSub { size 8{1} } = - ital "jC" rSub { size 8{1} } sqrt { { {b} over { \( ε rSub { size 8{r} } - 1 \) c} } } {} # h rSub { size 8{x} } = { {jε rSub { size 8{r} } k rSub { size 8{0} } Y rSub { size 8{0} } } over {ℓ rSub { size 8{0} } } } C rSub { size 8{1} } = ital "jY" rSub { size 8{0} } C rSub { size 8{1} } sqrt { { { \( ε rSub { size 8{r} } c+a \) ε rSub { size 8{r} } } over { \( ε rSub { size 8{r} } - 1 \) c} } } {} } } {}
alignl { stack { size 12{"The capacitance "C= { {C rSub { size 8{a} } C rSub { size 8{d} } } over {C rSub { size 8{a} } +C rSub { size 8{d} } } } " , "C rSub { size 8{a} } = { {ε rSub { size 8{0} } 2W} over {c} } ,C rSub { size 8{d} } = { {ε rSub { size 8{0} } ε rSub { size 8{r} } 2W} over {a} } } {} # C= { {ε rSub { size 8{0} } ε rSub { size 8{r} } 2W} over {ε rSub { size 8{r} } c+a} } {} # ital "LC"= { {ε rSub { size 8{0} } ε rSub { size 8{r} } μ rSub { size 8{0} } b} over {ε rSub { size 8{r} } c+a} } " "β=ω sqrt { ital "LC"} {} } } {}

---
alignl { stack { size 12{"The capacitance "C= { {C rSub { size 8{a} } C rSub { size 8{d} } } over {C rSub { size 8{a} } +C rSub { size 8{d} } } } " , "C rSub { size 8{a} } = { {ε rSub { size 8{0} } 2W} over {c} } ,C rSub { size 8{d} } = { {ε rSub { size 8{0} } ε rSub { size 8{r} } 2W} over {a} } } {} # C= { {ε rSub { size 8{0} } ε rSub { size 8{r} } 2W} over {ε rSub { size 8{r} } c+a} } {} # ital "LC"= { {ε rSub { size 8{0} } ε rSub { size 8{r} } μ rSub { size 8{0} } b} over {ε rSub { size 8{r} } c+a} } " "β=ω sqrt { ital "LC"} {} } } {}
alignl { stack { size 12{"Field expressions:"} {} # size 12{C rSub { size 8{2} } =C rSub { size 8{1} } "sin"ℓ rSub { size 8{0} } a/j"sinh"p rSub { size 8{0} } c approx - ital "jC" rSub { size 8{1} } βℓ rSub { size 8{0} } a/p rSub { size 8{0} } c} {} # 0 <= y <= a {} # e rSub { size 8{z} } =C rSub { size 8{1} } ℓ rSub { size 8{0} } y {} # e rSub { size 8{y} } = - { {jβ} over {ℓ rSub { size 8{0} } } } C rSub { size 8{1} } = - ital "jC" rSub { size 8{1} } sqrt { { {b} over { \( ε rSub { size 8{r} } - 1 \) c} } } {} # {} } } {}

---
alignl { stack { size 12{h rSub { size 8{x} } = { {jε rSub { size 8{r} } k rSub { size 8{0} } Y rSub { size 8{0} } } over {ℓ rSub { size 8{0} } } } C rSub { size 8{1} } = ital "jY" rSub { size 8{0} } C rSub { size 8{1} } sqrt { { { \( ε rSub { size 8{r} } c+a \) ε rSub { size 8{r} } } over { \( ε rSub { size 8{r} } - 1 \) c} } } } {} # "In the air region:" {} # e rSub { size 8{z} } =C rSub { size 8{1} } ℓ rSub { size 8{0} } a { { \( b - y \) } over {c} } {} # e rSub { size 8{y} } = - { {jβℓ rSub { size 8{0} } a} over {p rSub { size 8{0} rSup { size 8{2} } } c} } C rSub { size 8{1} } = - ital "jC" rSub { size 8{1} } ε rSub { size 8{r} } sqrt { { {b} over { \( ε rSub { size 8{r} } - 1 \) c} } } {} # h rSub { size 8{x} } = { {jk rSub { size 8{0} } Y rSub { size 8{0} } } over {ℓ rSub { size 8{0} } } } C rSub { size 8{1} } = ital "jY" rSub { size 8{0} } C rSub { size 8{1} } sqrt { { { \( ε rSub { size 8{r} } c+a \) ε rSub { size 8{r} } } over { \( ε rSub { size 8{r} } - 1 \) c} } } {} # V= - Int cSub { size 8{0} } cSup { size 8{b} } {e rSub { size 8{y} } } ital "dy"= ital "jC" rSub { size 8{1} } sqrt { { {b} over { \( ε rSub { size 8{r} } - 1 \) c} } } \( a+ε rSub { size 8{r} } c \) {} # I rSub { size 8{z} } =2 ital "WJ" rSub { size 8{z} } =2 ital "WH" rSub { size 8{x} } {} # {} # {} } } {}

---
size 12{"The characteristic impedance is:"} {}
alignl { stack { size 12{Z rSub { size 8{c} } = { {V} over {I} } = { {Z rSub { size 8{0} } } over {2W} } sqrt { { { \( a+ε rSub { size 8{r} } c \) b} over {ε rSub { size 8{r} } } } } = sqrt { { {L} over {C} } } } {} # "In the low frequency limit, the dominant mode of " {} # "propagation becomed a TEM mode " \( "quasi-TEM mode" \) {} # "At hight frequency the mode of propagation is an E mod" {} } } {}

---
Example:
Two plate transmission line
- Problems:
  - Plates are infinitely thin
  - Simulation mesh might get very big
- Solutions:
  - Define boundaries of inner square (or rectangle) as conductors
  - Pick appropriate size by trial and error, so that the simualtion results do not change drastically, compared with previous values

---
Calculating impedance
- We need L and C of the line
  - They are the part of the energy equations
  - Calculate them using these equations:
L = 2W_m over I^2
U = 2W_e over U^2
Optimization: set 1 for current and voltage in the simulation parameters

---
Calculating impedance...
The only step that is left now is:
Z = sqrt{L over C} = sqrt{2W_m over 2W_e} = sqrt{W_m over W_e}
- Then we can calculate the analytical function and compare the plots of two solutions
- In the formula above we consider I = 1A and U = 1V

---
Two parallel plates
- Consider following:
  - We have two infinitely thin plates of width w
  - They are separated by b meters of insulator
  - Let insulator be air
  - How impedance of such structure can be calculated?
  - Analytic formula:
Z approx %eta {b} over {w}
Fig. 1: Cross section of the line

---
Calculation results

---
Simulation screens
Fig. 2: Electric potential and its density in the two plate transmission line.
Fig. 3: Magnetic flux and its density in the two plate transmission line.

---
Some conclusions on case
- It can be seen from plot that the analytical formula is not always correct
- The bigger the plate width gets, the more accurate our estimation becomes
- The analytical formula approaches values of simulation, meaning that the error is decreasing and consequently getting closer to actual value

---
Wire above groung plane
Consider the following:
- An infinite charged plane
- A cable of diameter d above that plane
- Distance from center of the cable to the surface of the plane is h.
- Analytical formula for the impedance:
Z = %eta over {2 %pi} log{4h over w}
Fig. 4: Cross section of the line

---
Simulation and analytical solution

---
Future directions
- Fix simulations that were done improperly
- Make a proper report
- Reviev other cases (Shielded pair, for instance)
- Review different dielectrics (polyethylene, rubber)

---
COMSOL TIME
- Show some parts of the models in COMSOL
- Questions?